## Slide 1: E5IoT Project
Boiler-error IFTTT interface

## Slide 2: Project precursor
Wood-pellet boiler
  Used for house and utiliy water heating
  When error occurs, house heating is no longer
  effective after 15 minutes. Up to 160 liters of hot water is
  stored in utility tank, which can last between 2-24h
  if full.
LCD interface
Web interface
On error - both interfaces show an error, and a low
buzzer-alarm in the boiler is activated

## Slide 3: Problem overview
Boiler is located in basement, so there is no frequent supervision of boiler – in the future boiler will be moved to an entirely different building making supervision even more infrequent.
LCD and web interfaces also require manual monitoring to detect error
Boiler-rooms to have to comply with building regulations, as a consequence, sound is heavily dampened rendering buzzer useless as error detection.

## Slide 4: System requirements
Make error detection immediate (sensor)
Make error detection distractive, but not intrussive for users
Distinguish between error types
  Rutine errors – out of pellets, ignition error
  Critical errors – backburn, overheating (overtemperature), overcurrent
Integrate error notification into existing smarthome environment (actuator)

## Slide 5: Project feasibility study
Is it possible to extract necessary data from platform?
  Buzzer alarm
    This signal could easily be used as a flag for the particle to signal an error, but is unable to provide any information regarding error type.
  LCD decoder
    Reverse-decode signals sent to LCD, and compare to known error strings

## Slide 6: Project feasibility study
Is it possible to extract necessary data from platform?
  Web server data retrieval
    Ajax protocol parsing
      When inspecting the code running on the
      webserver, it showed an Ajax protocol is
      used to retrieve data from an XML document.
        Not being familiar with the Ajax protocol
        this option was dismissed after several
        attempts due to time-constraints.
    Further inspection into some of the
    references made in the initial code
    showed how the values on the web
    server main page are updated

## Slide 7: Project feasibility study
Is it possible to extract necessary data from platform?
  Error parsing
    The Ajax protocol parsing functions, while not being able to extract data, did show how the error codes should be parsed to make them human-understandable
    This showed how the error numbers codes are translated

## Slide 8: Project feasibility study
Is it possible to extract necessary data from platform?
  Having identified the errors, a given error could be provoked and the dataflow monitored to show where the error data was originating – this was traced to a file with the necessary data content.
  Note ”err1” flag

## Slide 9: Project feasibility study
Is it possible to extract necessary data from platform?
  Indeed the error given was verified both on the LCD and the web platform

## Slide 10: Project development
Create Github Repo - done
Create project in BB -
Using HTTPClient library to authenticate and get access to password protected webserver - done
HTTPClient also enables data retrieval – To do
Using particle.variable functions this data can be pushed to IFTTT Cloud – To do
IFTTT integration with Philips Hue bulbs and phone notification to provide user error-alerts – Needs analysis